## Slide 1
AERODRONE AI // AUTONOMOUS QUADCOPTER SIMULATION
Adaptive Neural Obstacle Avoidance with Synaptic Plasticity & Arduino Flight Control
Based on IEEE Research: Arne Devos, Emad Ebeid, Poramate Manoonpong (2018) 'Development of Autonomous Drones for Adaptive Obstacle Avoidance in Real World Environments' 21st Euromicro Conference on Digital System Design (DSD), DOI: 10.1109/DSD.2018.00009 Theoretical Foundation: Pedersen & Manoonpong (2018), LNAI (Two-Neuron RNN & Synaptic Plasticity) Implementation: 3D WebGL Simulation, 6-DOF Physics, Arduino C++ HITL Firmware, Human-in-the-Loop Decision Gate

## Slide 2
PROJECT MOTIVATION & PROBLEM DEFINITION
The Autonomous Drone Navigation Dilemma in Unknown Spaces
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
THE PROBLEM: VISION & SLAM COMPLEXITY
• Quadcopters operating in GPS-denied, cluttered spaces must navigate without human pilots.
• Environments contain unmapped obstacles, narrow passages, sharp corners, and dead-ends.
• Traditional solutions use Visual SLAM, deep CNNs, or heavy spinning 360° LiDARs.
• Heavy GPU compute platforms drain battery power and drastically shorten flight time.
• SLAM mapping easily fails in featureless, repetitive, or reflective indoor tunnels.
THE SOLUTION: ADAPTIVE NEURAL CONTROL
• Replaces heavy vision pipelines with an ultra-lightweight 2-neuron recurrent neural network.
• Operates on ONLY two narrow-beam (2°) LiDAR sensors mounted at front of frame.
• Short-Term Memory (STM): Retains turn command after obstacle exits laser field of view.
• Synaptic Plasticity: Adapts weights online to escape tight deadlocks and corners.
• Platform: Interactive 3D simulation, 6-DOF physics, and Arduino C++ HITL interface.

## Slide 3
BASE PAPER METHODOLOGY
Closed-Loop Neural Control Architecture (Devos et al. 2018)
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
METHODOLOGY & CLOSED-LOOP FLOW
• Published in IEEE 21st Euromicro Conference on Digital System Design (DSD 2018).
• Dual Garmin LIDAR-Lite v3 sensors measure obstacle range at 50 Hz.
• Raw distance normalized to [-1.0, +1.0] sensory inputs S_L and S_R.
• Discrete-time 2-neuron RNN with non-spiking tanh activation computes states O1, O2.
• Correlation plasticity modifies weights online based on sensor reflexes.
• Differential output generates yaw steering commanded to Pixhawk / Arduino via MAVLink.
PHYSICAL HARDWARE SYSTEM SPECIFICATIONS
• Frame: Tarot 650 Sport carbon-fiber quadcopter frame.
• Propulsion: 370 KV BLDC motors, 14" carbon props, 40A ESCs.
• Battery: 6S 22.2V 8000 mAh LiPo (25-minute flight endurance).
• Autopilot: Pixhawk 2 with 3D gyro, accelerometer, barometer, and PID loops.
• Companion SBC: Raspberry Pi Zero executing Python neural navigation.
• Distance Sensors: 2x Garmin LIDAR-Lite v3 (I2C interface, 2° beam).
• Protocol: MAVLink / MAVProxy / DroneKit serial command pipeline.

## Slide 4
MATHEMATICAL FOUNDATIONS
LiDAR Geometry & Minimum Detectable Obstacle Width
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
EQUATION (1) & GEOMETRIC FORMULATION
• To guarantee safety, minimum detectable obstacle width W_obj is governed by Equation (1):
W_obj ≥ 2 · tan(Θ / 2) · [ Lx + (Ld / 2) ]
• Θ (LiDAR Separation Angle): 40° total angle (±20° relative to forward axis).
• Lx (Safe Turning Distance): 0.15 m (15 cm) turning threshold.
• Ld (Quadcopter Frame Width): 0.34 m (34 cm) rotor-to-rotor span.
• Lm (Rotor Safety Margin): 0.06 m (6 cm) propeller clearance.
• Ls (Max LiDAR Range): 0.50 m (50 cm) active detection horizon.
ANALYTICAL DERIVATION & SAFETY GUARANTEES
• Evaluating Equation (1) with base paper parameters:
tan(20°) ≈ 0.36397
Lx + (Ld / 2) = 0.15 + 0.17 = 0.32 m
W_obj ≥ 2 · 0.36397 · 0.32 m = 0.2329 m ≈ 24 cm
• Any obstacle ≥ 24 cm is guaranteed to be detected before drone is within 15 cm.
• All obstacles across our scenarios have widths ≥ 24 cm matching paper rigor.
• Minimum Clearance Boundary: Lm + Ld/2 = 0.23 m (rotor collision threshold).

## Slide 5
SENSORY PROCESSING PIPELINE
LiDAR Range Normalization & Sensory Input Mapping
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
NORMALIZATION EQUATION & TRANSFER FUNCTION
• Raw distance readings d_L, d_R mapped into bipolar normalized signals:
S_i = clip( [ 2 · (d_max - d_i) / (d_max - d_min) ] - 1.0, -1.0, 1.0 )
• d_max = 0.50 m (sensing range Ls); d_min = 0.15 m (critical turning dist Lx).
• S_i = -1.0: Clear airspace (d_i ≥ 0.50 m), zero reflex excitation.
• S_i = 0.0: Transition boundary (d_i = 0.325 m), reflex begins activating.
• S_i = +1.0: Critical proximity (d_i ≤ 0.15 m), maximum excitatory turning drive.
DUAL SENSOR ARRANGEMENT & 3D EXPANSION
• Left LiDAR (S_L): Oriented at +20° azimuth relative to drone heading.
• Right LiDAR (S_R): Oriented at -20° azimuth relative to drone heading.
• Narrow 2° beam eliminates ground bounce and multipath interference.
• 3D Simulation Expansion: Adds 8 planar radial raycast beams (0° to 315°)
plus vertical ceiling and ground laser sensors.
• Feeds multi-directional clearance telemetry to Human-in-the-Loop decision gate.

## Slide 6
BIO-INSPIRED NEURAL CONTROL
Two-Neuron Recurrent Network with Mutual Inhibition
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
RECURRENT STATE UPDATE EQUATIONS
• Discrete-time non-spiking neural equations with tanh activation:
O_1(t) = tanh( b_1(t)·O_1(t-1) + c(t)·O_2(t-1) + I_g·S_L(t) )
O_2(t) = tanh( b_2(t)·O_2(t-1) + c(t)·O_1(t-1) + I_g·S_R(t) )
• O_1, O_2 ∈ (-1.0, 1.0): Left and Right neuron activation states.
• O_1(t-1), O_2(t-1): Prior activations providing Short-Term Memory.
• b_1, b_2 ∈ [0.1, 8.0]: Self-excitatory recurrent synapses (baseline = 2.40).
• c(t) = -0.5 · [ q_1(t) + q_2(t) ]: Mutual inhibitory cross-coupling (baseline = -3.50).
• I_g = 4.7: Sensory input gain scaling LiDAR inputs.
NEURAL COMPETITION & EFFICIENCY ADVANTAGES
• Left obstacle stimulates S_L ==> O_1 excites, cross-inhibits O_2 ==> Sharp Right turn.
• Right obstacle stimulates S_R ==> O_2 excites, cross-inhibits O_1 ==> Sharp Left turn.
• Symmetrical inputs broken instantly by historical turning bias and memory.
• Only 4 adaptable synaptic weights vs millions in modern deep learning models.
• Sub-microsecond execution time on microcontroller platforms.
• Requires zero pre-training: operates completely online in closed-loop.

## Slide 7
ONLINE ADAPTATION
Correlation Plasticity & Synaptic Scaling for Deadlock Escape
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
THE DEADLOCK PROBLEM & PLASTICITY EQUATIONS
• In corners and deadlocks, turning sweeps the obstacle out of narrow 2° LiDAR beams.
• Without plasticity, the drone stops turning too early and collides with walls.
• Online Correlation Plasticity (Pedersen & Manoonpong 2018):
v_i(t) = clip( [ O_i(t) + 1 ] / 2, 0.0, 1.0 )
reflex_i(t) = 1.0 if S_i(t) > -0.5 else 0.0
Δb_i = κ·Δt · [ μ_b·v_i(t-1)·v_i(t)·reflex_i + γ_b·(k - v_i)·b_i² ]
Δq_i = κ·Δt · [ μ_q·v_i(t-1)·v_i(t)·reflex_i + γ_q·(k - v_i)·q_i² ]
HYPERPARAMETERS & DUAL-PHASE ADAPTATION
• Scaling rate κ = 27.0; Learning rates μ_b = 0.0065, μ_q = 0.015.
• Homeostatic decay rates γ_b = 0.0003, γ_q = 0.0003; Target baseline k = -0.01.
• Hebbian Potentiation (1st term): Increases b_i and q_i during reflex, prolonging memory.
• Homeostatic Scaling (2nd term): Relaxes weights to baseline in open air.
• Enables drone to complete 90° and 180° turns without getting stuck in corners.
• Base Paper Result: 90% to 100% autonomous escape success in complex deadlocks.

## Slide 8
FLIGHT DYNAMICS & CONTROL
Yaw Steering Calculation & Proximity Velocity Regulation
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
YAW RATE COMMAND GENERATION
• Steering command is calculated from neural differential:
steering(t) = 0.5 · [ O_1(t) - O_2(t) ]
ψ̇_cmd(t) = -k_turn · steering(t) (k_turn = 1.35 rad/s)
• Left Obstacle (S_L > S_R): steering > 0 ==> ψ̇_cmd < 0 (Turn Right).
• Right Obstacle (S_R > S_L): steering < 0 ==> ψ̇_cmd > 0 (Turn Left).
• Proportional turning speed enables smooth evasive bank angles.
VELOCITY REGULATION & FLIGHT DYNAMICS
• Forward velocity throttles down when approaching obstacles:
V_f = 0.00 m/s if S_L > 0.55 and S_R > 0.55 (Head-on Deadlock)
V_f = 0.025 m/s if max(S_L, S_R) > 0.25 (Very Close)
V_f = 0.055 m/s if max(S_L, S_R) > -0.15 (Approaching)
V_f = 0.10 m/s otherwise (Nominal Forward Cruise)
• 6-DOF physics models drag, lift, rotor inertia, and coordinated turns.
• Velocity throttling ensures turn radius fits within available clearance.

## Slide 9
EMBEDDED HARDWARE & FIRMWARE
Tarot 650 Quadcopter & Arduino Flight Controller Firmware
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
ARDUINO C++ FIRMWARE FEATURES
• Included firmware: arduino/arduino_flight_controller.ino for Mega 2560 / Uno / ESP32.
• 4-Channel ESC PWM pulse generation (D5, D6, D9, D10) at 50 Hz.
• Dual ultrasonic / LiDAR distance sampling matching base paper timing.
• Cascaded PID flight stabilization: Inner rate PID + Outer angle PID.
• X-quadcopter motor mixing matrix (Roll, Pitch, Yaw, Throttle).
• Safety failsafe: Disarms motors on communication timeout or emergency stop.
HITL/SITL SERIAL PROTOCOL & DUAL MODES
• Bidirectional ASCII telemetry: $TELEM, dL, dR, roll, pitch, yaw, armed, estop.
• Hardware-in-the-Loop (HITL): Connects physical Arduino via USB serial COM port.
• Software-in-the-Loop (SITL): Simulates Arduino firmware transparently when unplugged.
• Physical airframe: Tarot 650 Sport, 370 KV motors, 14" stiff props, 40A ESCs, 6S LiPo.
• Companion bridge: serial_bridge.py handles UART communications at 115200 baud.

## Slide 10
OPERATOR INTERACTION & SAFETY
Human-in-the-Loop (HITL) Obstacle Avoidance Workflow
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
7-STAGE DECISION PIPELINE
• Cruising: Quadcopter cruises forward at 0.10 m/s at Z = 1.0 m hover altitude.
• Detection: Sensor detects obstacle within 0.50 m threshold.
• Simulation Pause: Simulation clock halts forward progression automatically.
• Safe Hover: Quadcopter holds stable hover in WAITING_FOR_USER state.
• Safety Audit: Evaluates clearance across all 10 candidate evasion directions.
• Operator Choice: User clicks direction or presses hotkey (W, A, S, D, Q, E, etc.).
• Execution & Logging: Drone executes maneuver, updates trajectory, and logs trial.
SAFETY AUDIT & RESEARCH OVERRIDE
• RECOMMENDED: Optimal base-paper neural evasion direction (Green).
• SAFE: Clearance > 0.50 m, open airspace.
• CAUTION: Clearance 0.23 m - 0.50 m, restricted corridor.
• BLOCKED: Clearance < 0.23 m (rotor collision threshold). Blocked by default.
• Research Override Switch: Enables operators to test unsafe decisions deliberately
to inspect collision physics and damage telemetry for comparative research.

## Slide 11
FULL-STACK DASHBOARD ARCHITECTURE
Interactive 3D Simulation & Real-Time Telemetry Dashboard
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
3D VIEWPORT & VISUALIZATION
• Web dashboard running on http://localhost:8080 with Three.js WebGL.
• Realistic Tarot 650 quadcopter model with spinning rotors and status LEDs.
• Real-time LiDAR laser beams with impact hit markers (Green/Yellow/Red).
• Continuous 3D flight trajectory ribbon tracing evasion paths.
• 4 Camera Modes: Chase Drone, Free Orbit, Tactical Top-Down, FPV Nose Cam.
CONTROLS, HOTKEYS & TELEMETRY
• 10 Direction Buttons: Forward, Backward, Left, Right, Up, Down, 4 Diagonals.
• Full Keyboard Shortcuts: W/A/S/D, Q/E/Z/C, R/F, Space (Start/Pause), Enter, Esc.
• Dual Pilot Modes: Instant switch between Autonomous Devos (2018) and Manual Pilot.
• Live Telemetry HUD: Altitude, Airspeed, Yaw Heading, Clearance meters.
• Neural Network Monitor: Real-time values of O1, O2, b1, b2, q1, q2, and plasticity.
• Speed Multipliers: 0.5x, 1.0x, 2.0x, 5.0x simulation clock control.

## Slide 12
VALIDATION ENVIRONMENTS
Comprehensive 13-Scenario Obstacle Avoidance Library
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
DIRECTIONAL & GEOMETRIC TEST SUITE
• 1. front_obstacle: Front pillar; lateral evasion.
• 2. right_obstacle: Right flank wall; leftward evasion.
• 3. left_obstacle: Left flank barrier; rightward evasion.
• 4. rear_obstacle: Reverse threat; forward braking.
• 5. above_obstacle: Overhead bridge; vertical descent.
• 6. below_obstacle: Raised platform; vertical climb.
• 7. both_sides: Lateral pinch; reverse/vertical escape.
DIAGONAL, CLUSTER & MAZE SCENARIOS
• 8. front_left: 45° diagonal threat; front-right evasion.
• 9. front_right: -45° diagonal threat; front-left evasion.
• 10. rear_diagonal: Rear diagonal quadrant threats.
• 11. multiple_obstacles: Dense field of 7 pillars and boxes.
• 12. paper_env2_maze: Devos et al. Fig 5(b) Complex Maze.
• 13. clear_flight: Open airspace baseline.
• Note: Narrow corridor, moving obstacle, and env 1 removed per user request.

## Slide 13
ACADEMIC INTEGRITY & RIGOR
Distinction Between Base Paper Ground Truth & Simulation Features
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
BASE PAPER SPECIFICATIONS
• Dual front LiDARs in 2D horizontal plane.
• Continuous autonomous reactive closed-loop control.
• Yaw steering only (Turn Left / Right).
• V-REP robotics simulator with C++ ROS bridge.
• Pixhawk 2 + Raspberry Pi Zero companion SBC.
• 2 static test environments (Room & Maze).
• Qualitative trajectory observation.
SIMULATION PLATFORM IMPLEMENTATION
• Exact dual front LiDARs + 8 radial raycasters + Up/Down 3D sensors.
• Interactive Human-in-the-Loop decision gate with safe hover and safety audit.
• 10 directional degrees of freedom (horizontal, vertical, diagonal).
• 6-DOF Quadcopter Physics + Three.js 3D WebGL Dashboard at 30 Hz.
• Python neural controller + Arduino C++ firmware with SITL/HITL.
• 13 scenarios covering all spatial threat angles.
• Real-time automated logging with one-click export to CSV and JSON.

## Slide 14
EXPERIMENTAL EVALUATION
Telemetry Logging, Experiment Analytics & Performance Metrics
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
DATA COLLECTION & LOGGING SCHEMA
• Every trial records Trial ID, Scenario ID, and initial/final positions.
• Captures full sensory snapshot at detection trigger moment.
• Logs available safe directions, user selection, and override status.
• Measures human/controller response time latency (seconds).
• Measures minimum obstacle clearance throughout entire evasion path.
• Records trial outcome: SUCCESS, COLLISION, or TIMEOUT.
QUANTITATIVE METRICS & BENCHMARKS
• Success Rate (%): Percentage of trials avoided without collision.
• Collision Rate (%): Impact occurrences during research override testing.
• Mean Response Time (s): Average operator decision latency.
• Minimum Clearance (m): Closest point of approach during maneuver.
• Base Paper Benchmark: 100% low density, 90% high density, 90% deadlocks.
• Instant Data Export: Downloadable CSV (/api/logs/csv) and JSON (/api/logs/json).

## Slide 15
SOFTWARE ARCHITECTURE
Directory Structure, Codebase Modules & Automated Test Suite
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
PROJECT DIRECTORY & MODULES
• main.py: aiohttp async web server, 30 Hz physics loop, WebSocket hub.
• simulation/: drone_physics.py, scenarios.py, experiment_logger.py.
• avoidance/: neural_controller.py (RNN + plasticity), decision_engine.py.
• sensors/: lidar_sensor.py (dual front LiDAR + 3D raycasting).
• dashboard/: index.html, style.css, three_sim.js, app.js.
• arduino/: arduino_flight_controller.ino, serial_bridge.py.
• scenarios/: 13 JSON scenario definition files.
• tests/: Comprehensive automated pytest unit test suite.
AUTOMATED UNIT TESTING & VERIFICATION
• test_avoidance.py (7 tests): Normalization bounds, tanh neuron states, steering signs, synaptic plasticity adaptation, and HITL state machine.
• test_physics.py (4 tests): 2D circle/box intersection math, 6-DOF translation dynamics, and collision boundary detection.
• test_scenarios.py (3 tests): Library completeness, CSV/JSON logging, and steps through all 13 scenarios with 0 collisions.
• Execution: python -m pytest tests/ ==> 14/14 tests pass.
• Live Server: http://localhost:8080/ (running continuously in background).

## Slide 16
CONCLUSIONS & OUTLOOK
Summary of Achievements, Research Impact & Future Work
Autonomous Quadcopter Obstacle Avoidance Simulation | Devos et al. (2018) IEEE DSD
SUMMARY OF CONTRIBUTIONS
• Faithful Research Reproduction: Implemented equations, parameters, and RNN dynamics from Devos et al. (2018) and Pedersen & Manoonpong (2018).
• Ultra-Low Compute Footprint: Proved deadlocks are resolved using only 2 neurons, 4 weights, and dual lightweight LiDARs.
• Validated Geometric Bounds: Verified Equation (1) with W_obj ≥ 24 cm for 15 cm turning thresholds.
• Interactive Human-in-the-Loop Platform: Combined autonomous neural control with operator decision verification.
• Hardware-Ready Arduino Firmware: Provided complete C++ flight controller code and SITL/HITL bridge.
FUTURE WORK & PROJECT ACCESS
• Physical flight validation on Tarot 650 quadcopter in real-world tunnels.
• ROS 2 Humble micro-XRCE-DDS integration for multi-agent swarm coordination.
• Dynamic obstacle trajectory prediction in non-stationary environments.
• Distributed neural consensus among quadcopters in shared corridors.
• Live Simulation Link: http://localhost:8080/
• 13 active scenarios, full keyboard controls, and real-time telemetry logging.